## Slide 1
URBAN MOBILITY CHALLENGE
Alessandro Borgherini - 2123456
Riccardo Rettore - 2110512
Thomas Zamprogno - 2121463

## Slide 2: Outline
Introduction & Objectives
Framework
Obstacle avoidance procedure
Trajectory tracking control
  State error feedback controller
    Linear control
    Nonlinear control
  Output error feedback controller
    B-point control
    Further derivatives control
Parking
  Cartesian regulation
  Posture regulation

## Slide 3: Introduction: the "urban mobility challenge"
Problem: An autonomous guided vehicle (AGV) has to travel along a closed circuit avoiding the other AGVs that are parked along the path; at the completion of one lap, the AGV has to get off the circuit and park at the box
PROJECT OBJECTIVES:
Track a closed-loop trajectory
Avoid obstacles on the trajectory
After performing one lap, reach an empty parking lot
PROPOSED SOLUTIONS:
State & output error feedback
Sensor for obstacle detection and avoidance
Cartesian & Posture regulation

## Slide 4: Framework: unicycle
y
x
θ
The AGV used in the project is a unicycle robot, a planar vehicle with a single orientable wheel

## Slide 5: Framework: trajectory
To design the desired trajectory, a series of waypoints was defined. These waypoints were then interpolated using cubic spline interpolation to ensure a continuous path
To test controllers' functionalities on a non-continuous path, a sharp square-angle turn is added to the path

## Slide 6: Obstacle avoidance
The unicyle after detecting the obstacle progressively reaches the second lane, after overtaking the obstacle it progressively returns to the first lane
To ensure a smooth and continuous trajectory during the changing lane procedure a sigmoid function has been used

## Slide 7: Obstacle avoidance

## Slide 8: Parking problem
Two waypoints for the parking
Simulate a real parking condition

## Slide 9: Merger between the tracking trajectory and the parking
Enable to activate individual phases
Automatic switching

## Slide 10: TRAJECTORY TRACKING - STATE ERROR FEEDBACK

## Slide 11: Design
controller
! Constraints on the trajectory !
twice differentiable
and feasible for the unicycle

## Slide 12
Differential Flatness
avoiding division by zero

## Slide 13: Linear Control

## Slide 14
Controller design
saturation
TI
TV
no guarantee of asymptotic stability,
only for rectilinear and circular motion
persistent trajectories
Eigs allocation:

## Slide 15
X TRACKING
Y TRACKING
Plots

## Slide 17
FOCUS ON SQUARE CORNER

## Slide 19: Nonlinear Control
dynamic of the errors is in mixed form

## Slide 20
Controller design
nonlinear term
no more singularity in vd=0
assuming (vd,wd) bounded with bounded derivatives
and (vd,wd) do not go concurrently to zero
TV
TI
resembles k2 of the linear controller
global asymptotic stability
square curve

## Slide 21
Plots
X TRACKING
Y TRACKING

## Slide 23
FOCUS ON SQUARE CORNER

## Slide 25
changing desired dumping and b:
d = 2 / sqrt(2)
b =1
Less aggressive , more stable

## Slide 26
d = 2 / sqrt(2)
b =1

## Slide 28
d = 2 / sqrt(2)
b =1
d = 1 / sqrt(2)
b =10
d = 1 / sqrt(2)
b =10
d = 2 / sqrt(2)
b =1

## Slide 29: TRAJECTORY TRACKING - OUTPUT ERROR FEEDBACK

## Slide 30: Feedback linearization based on a reference point on the sagittal axis

## Slide 31
Map

## Slide 32
Controller design
Pro:

## Slide 33
Plot

## Slide 35
Plot
b small:
Better trajectory
b large:
A smoother trajectory

## Slide 36
Plot
b small:
Higher rotational speed
b large:
Less rotational speed

## Slide 38: Feedback linearization based on second order derivatives

## Slide 39
Map
It prevents singularity due to the angle at 90° with v=0

## Slide 40
Controller design
Need:
PD

## Slide 41
Plot

## Slide 42
Plot

## Slide 44: REGULATION

## Slide 45: Cartesian regulation

## Slide 46
Control law

## Slide 47
Plot
Proportional trend
The error tends to zero, resulting in lower speed
The greater the error, the greater the speed action

## Slide 48
Plot
Overshoot 2.58%

## Slide 49
Gains
Overshoot [2, 1.5, 1.2] %
Final position in [0.15, 0.25, 0.45] s

## Slide 51: Posture regulation (1° version)
Convert to polar coordinates

## Slide 52
State trasformation
polar coordinates

## Slide 53
Control law
New term
At starting time is 0
Problem:potential singularity when ρ=0

## Slide 54
Plot
Final position in [0.17, 0.5, 1.3] s

## Slide 55
Plot
Lenght from the origin
!

## Slide 56
Plot
V is modulated based on the distance from the origin
High speed far from the origin
Greater precision with lower speed when close to the origin.

## Slide 57: Posture regulation(with singularity)

## Slide 58: Posture regulation (2°version)
Avoid singularity on ρ with change of input
New:

## Slide 59
New Control law

## Slide 60
Plot
Reaches final position in 0.5 s
The concave shape is given by the fact that the linear velocity is proportional to roh

## Slide 61
Plot
Final position in [0.17, 0.5, 1.3] s

## Slide 62
Plot

## Slide 63: Posture regulation (without singularity)

## Slide 64: Final considerations - tracking
State error feedback
Works with the state (x,y,theta)  theta directly controlled
Trajectory must be twice differentiable and persistent
Differential Flatness block induces constraints on the trajectory
System dynamic is coupled
Controller design is more complicated than the others, gains are time varying and related to the velocities
Convergence is difficult to guarantee (linear  only locally, nonlinear  only with bounded velocities and bounded derivatives)
Output error feedback , B-point
Theta is not directly controlled, but coupled in the dynamics with x and y
It works with any trajectories, given in terms of xb and yb, so no smooth constraints (as far as b!=0)
The dynamic becomes linear,decoupled, SISO , single integrator
Control design is easy, PD with gains TI and > 0
Output error feedback , further derivatives
Same as diff flatn, trajectory must be smooth (differentiable) and persistent , v!=0 (singular mapping)
System dynamic becomes decoupled, linear, double integrator
Controller design is quite easy, gains TI and >0 (but there are 4 gains)
BEST AMONG THE FOUR

## Slide 65: Final considerations - regulation
Cartesian regulation
Theta non controlled
v proportional to ep
Controller design simple, 2 gains > 0
No singularities issues
Posture regulation
Theta is now controlled but indirectly (through gamma and delta)
Controller design is more difficult, 3 gains and gamma at the denom (even if there is semplification in case)
Singularity problem in rho=0  solved by shifting singularity in input

## Slide 66: Output error feedback (B-point) and posture regulation(without singularity)