## Slide 1
Unicycle project

## Slide 2: Outline
Introduction
Framework
Diff. Flatn L & NL
Output state
parking

## Slide 3: Introduction: the "urban mobility challenge"
Problem: An autonomous guided vehicle (AGV) has to travel along a closed circuit avoiding the other AGVs that are parked along the path; at the completion of one lap, the AGV has to get off the circuit and park at the box
PROJECT OBJECTIVES:
Track a closed trajectory
Avoid obstacles on the trajectory
After performing one lap, reach an empty parking lot

## Slide 4: Framework: unicycle
The AGV used in the project is a unicycle, a planar vehicle which is described by its state
y
x
θ

## Slide 5: Framework: trajectory
To design the desired trajectory, a series of waypoints was defined. These waypoints were then interpolated using cubic spline interpolation to ensure a continuous path
To test controllers' functionalities on a non-continuous path, a sharp square-angle turn is added to the path

## Slide 6: Obstacle avoidance
The unicyle after detecting the obstacle progressively reaches the second lane, after overtaking the obstacle it progressively returns to the first lane
To ensure a smooth and continuous trajectory during the changing lane procedure a sigmoid function has been used

## Slide 7: Obstacle avoidance

## Slide 8: TRAJECTORY TRACKING - STATE ERROR FEEDBACK

## Slide 9: Linear case
Notes: THINGS TO SAY:
General overview of the structure
Vdes != 0 , so persistent trajectory (even more important later on with k2 (v is at the denom)
w depends on v^2 basically, so we must have v !=0, furthermore later on , k2=num/vd so vd!=0 otherwise k2 explodes, we will add a saturation on it
We can not guarantee asymp convergence cause system TV, but we do have convergence property cause we are doing rectilinear and semicircular motions so someway we are covered by good convergence properties
explain the wrap / unwrap:
  we used the unwrap to normalize theta angle, so we don't have the discontinuity going from 2pi to 0

## Slide 10
Avoiding division by zero
differential flatness block

## Slide 11
Controller design
Notes: Say something about eigenvalues, thanks to this ki we know the eigs are on the LHS

## Slide 14
Focus on sharp curve
differential flatness block should not be able to compute the input velocities when reaching a non differentiable part of the trajectory. Indeed, impulses in both velocities arises, with stronger effect in omega, (its computation is based on the second order derivative).
Nonetheless, thanks to saturator blocks on omega and gains we are able to overcome the problem and to finish the simulation anyway.

## Slide 15: Video
Sistemare e tagliare video

## Slide 16: Non Linear case
Notes: THINGS TO SAY:
General overview of the structure and vdes!=0  same as before cause its related with diff flatness
Highlights the same nature of the structure, with the only difference : gain computation and feedback law
Barbalat’s lemma problem. Before we had no convergence guarantees cause k2 TV , now instead we could end up with loosing conv property cause w could become unbounded and hence Barb no true anymore - this is what we stress out in the sharp curve
explain the wrap / unwrap:
  we used the unwrap to normalize theta angle, so we don't have the discontinuity going from 2pi to 0

## Slide 17
Controller design
Notes: Highlight the relation between a and b , could we also compute eigs for this ? Is b a natural freq too ?

## Slide 19
Plots --> see if impulse bigger than linear case follows some theoretical thing or just related to gains tuning

## Slide 20
Focus on sharp curve
Make a consideration regarding NL more enhanced wrt lineare case, maybe theres a reason

## Slide 21: Video
Sistemare e tagliare video

## Slide 22
Confronto tra linear e non linear nella zona sorpasso
+
Confronto tra linear e non linear nella zona curva a 90

## Slide 23
Qualche breve considerazione finale sui due controllori, che poi verrà ripresa meglio alla fine della presentazione

## Slide 24: TRAJECTORY TRACKING - OUTPUT ERROR FEEDBACK

## Slide 25: Feedback linearization based on a reference point on the sagittal axis

## Slide 26
Map

## Slide 27
Controller design
Pro:

## Slide 28
Plot

## Slide 29: Feedback linearization based on second order derivatives

## Slide 30
Map

## Slide 31
Controller design
Need:

## Slide 32
Plot

## Slide 33
Plot

## Slide 34: REGULATION

## Slide 35: Cartesian regulation

## Slide 36
Control law

## Slide 37: Pose regulation

## Slide 38
State trasformation

## Slide 39
Control law

## Slide 40: Plots of all controllers together